Annexure 3

ISO 8217: 2005

Table 1 – Requirement for marine distillate fuels

| Characteristic | Unit | Limit | Category ISO-F DMA | Test method reference |
| --- | --- | --- | --- | --- |
| Density at 15 oC | Kg/m3 | max | 890.0 | ISO 3675 or ISO 12185 |
| Viscosity at 40 oC | mm2/s | min max | 1.50 6.00 | ISO 3104 ISO 3104 |
| Flash point | oC | min | 60 | ISO 2719 |
| Pour point (upper) Summer | oC | max | 0 | ISO 3016 |
| Sulphur | %(m/m) | max | 0.10 (max) | ISO 8754 or ISO 14596 |
| Cetane index | - | min. | 40 | ISO 4264 |
| Carbon residue On 10% (v/v) distillation Bottom Carbon residue | %(m/m) %(m/m) | max max | 0.30 - | ISO 10370 ISO 10370 |
| Ash | %(m/m) | max | 0.01 | ISO 6245 |
| Appearance | - | - | Clear & bright Colour Max ASTM No. 3 |  |
| Total sediment, existent | %(m/m) | max | - | ISO 10307-1 |
| Water | %(V/V) | max | - | ISO 3733 |
| Vanadium | mg/kg | max | - | ISO 14597 or IP 501 or IP 470 |
| Aluminium plus silicon | mg/kg | max | - | ISO 10478 or IP 501 or IP 470 |

Metals to report

NOTE : Fuel shall be free of Used Lubricating Oil (ULO)

The Test Method shall be ISO or relevant ASTM method.

ISO 8217: 2017

Table 2 – Requirement for marine residual fuels

| Characteristic | Unit | Limit | RMG 380 | Test method reference |
| --- | --- | --- | --- | --- |
| Density at 15 oC | Kg/m3 | max | 991.0 | ISO 3675-1998 |
| Kinematic viscosity at 50 oC | cSt | max | 380 | ISO 3104-1994 |
| CCAI | - | max | 870 | Calculated |
| Flash point | oC | min | 60.0 | ISO 2719-2002 |
| Hydrogen Sulfide | mg/kg | max | 2.00 | IP 570B |
| Acid Number | mgKOH/g | max | 2.5 | ASTM D664-18E2 |
| Pour point (upper) -winter quality -summer quality | oC | max max | 30 30 | ISO 3016-1995 ISO 3016-1995 |
| Carbon residue-Micro method | mass% | max | 18.00 | ISO 10370-1993 |
| Ash | mass%) | max | 0.100 | ISO 6245-2001 |
| Water | Vol % | max | 0.50 | ISO 3733-1999 |
| Sulfur | mass% | max | 0.5 | ISO 8754-2003 |
| Vanadium (V) | mg/kg | max | 350 | IP 501/05 |
| Sodium (Na) | mg/kg | max | 100 | IP 501/05 |
| Total sediment Potential | mass% | max | 0.10 | ISO 10307-01-1993 |
| Aluminium plus sillicon | mg/kg | max | 60 | IP 501/05 |
| Used lubricating oil (ULO) Calcium (Ca) and Zinc (Zn) Or Calcium (Ca) and Phosphorus(P) | mg/kg |  | Ca>30 & Zn>15 Or Ca>30 & P>15 | IP 501/05 |

Metals to report

NOTE : Fuel shall be free of Used Lubricating Oil (ULO)

The Test Method shall be ISO or relevant ASTM method.